关键词

Lockbolt,lockpin,lock collar,huck bolt

归类需要根据每个网站的不同特别来分，自己找找就行，一般有交通、汽车、工业、五金等字眼就可以选择。

Product Description:

1. Material:Carbon steel,Aluminium,Stainless Steel,.

2. Surface Treatment: Zinc  Plated,Black Phosphated

3.Size:3/16”,1/4”,5/6”,3/8”,1/2”,5/8”,3/4”,7/8”,1”,1-1/8”.

4. Pin Type: Flat Round Head,90º Fiush Head,Truss Head,countersunk head.

5.Collar Type:Standard,flange.

6.Packaging: cartons&pallets.

7.Shipping:As your request.

8.Delivery: Within 30 days upon confirming your order.

9.Application: used for a wide range of applications such as vehicle, railway, wagon, bridge, construction, aviation, container, mining, large-scale steel structure, electrical establishment etc.

We mainly sell the lockbolts to railway, the manufacturer of wagon, heavy truck, mining industry. (Such as Chinese railway, Indian railway, TATA, BOLOGNESI,GM etc.)

Application:

vehicle, railway,

wagon, bridge, construction, aviation, container, mining, large-scale steel structure, electrical establishment etc.

- 材质：铁，铝，不锈钢。

- 表面处理：电镀，发黑。

- 尺寸：3/16，1/4，5/6，3/8，1/2，5/8，3/4，7/8，1，1-1/8。

- 铆钉类型：半圆头，沉头，大扁圆头。

- 环套类型：标准，法兰。

- 包装：纸箱，托盘。

- 发货：根据客户需求。

- 交货期：根据确认的订单可以在15天交货。

- 产品应用：广泛用于汽车，铁路，货车，桥梁，建筑，航空，集装箱，矿山，大型钢结构，电气设施等领域。

我们主要把环槽铆钉卖给铁路公司，汽车制造商，重型卡车，采矿业。（例如中国铁路，印度铁路，塔塔，博洛尼，通用等）。

我们的服务：

不同材料的各种款式

大库存尽快装运

高品质价格优廉

样品或小订单都可以

可靠的质量保证

最好的销售服务

富有出口经验

1.环槽铆钉:也叫哈克钉,一套环槽铆钉由一个铆钉和一个环套组成的,具有高强度夹紧力和防震功能,能够替代常规的螺栓螺母。它是通入夹紧板面的两边来进行安装,比一般铆钉提供更高的剪切力、抗拉强度和抗振性。

工作原理:环槽铆钉经由哈克枪在单向拉力的作用下,拉伸铆钉并推挤套环,将环套挤压到大牙内使环套和铆钉100%结合,产生永久性紧固力。

C50L环槽铆钉直径范围为:1/2英寸(公制M13)、5/8英寸(公制M16)、3/4英寸(公制M20)、7/8英寸(公制M22)、1英寸(公制M25)、1-1/8英寸(公制M28).铆接范围从6.35mm开始,根据客户实际生产需要定制。环槽铆钉被誉为永不松动的紧固件,其拥有高强度的抗拉力、剪切力,有很好的抗震性和防盗性,被广泛运用于震动筛机械、矿山机械、铁路、轨道、桥梁、机车等重工业高风险行业。

我司99%的环槽铆钉业务均是出口,各直径各铆接长度均常年备有库存,交货期快成为我们最大的竞争优势。我司产品品质能够与HUCK,AVDEL相当,所有环槽铆钉我司都从产品外形尺寸到产品硬度、拉断力、抗拉力以及铆接测试进行全面的检测管控。产品出口美国墨西哥铁路、机车制造企业多年,从未收到任何质量投诉。

2.用途： 用于铆接两个结构件使之成为一件整体。由铆钉和钉套两个零件组成。铆钉的钉体（直径D部分）一端连接钉头，另一端连接两段环槽的钉杆，钉杆靠近铆钉钉体的 一段为工作段环槽，远离铆钉钉体的一段为夹持段环槽。铆接时，先将铆钉插入被连接件的钉孔中，再从被连接件另一面将钉套套在铆钉的工作段环槽上，然后用专 用工具---气动环槽铆钉枪的枪口套在铆钉的夹持段环槽上，旺发牌]并将枪口抵住钉套端面，再扣动枪上扳机，铆钉枪即将铆钉的夹紧段环槽钉杆拉紧，直到断裂为止。 此时，钉套内壁挤入铆钉的工作段环槽中，形成新铆钉头，从而把被连接件铆接紧固。其特点是：操作方便，效率高，噪声低，抗震性好，故广泛用于各种车辆，船 舶，航空，机械设备，建筑结构等领域中。

3.【环槽铆钉】用于铆接两个结构件使之成为一件整体。由铆钉和钉套两个零件组成。铆钉由钉杆和钉套组成。铆接时，先将铆钉插入被连接件的钉孔中，再从被连接件另一面将钉套套在铆钉的工作段环槽上，然后用专用工具---气动环槽铆钉枪的枪口套在铆钉的夹持段环槽上，并将枪口抵住钉套端面，再扣动枪上扳机，铆钉枪即将铆钉的夹紧段环槽钉杆拉紧，直到断裂为止。此时，钉套内壁挤入铆钉的工作段环槽中，形成新铆钉头，从而把被连接件铆接紧固。其特点是：操作方便，效率高，噪声低，抗震性好，故广泛用于各种车辆，船舶，航空，机械设备，建筑结构等领域中。

4.环槽铆钉又名哈克钉、是一种新型的高强度紧固件、振动筛子用环槽铆钉是一种高科技产品、它经过精车退火，调质及多种工序精制而成、主要用于大、中型振动筛上长期应用，钢结构环槽铆钉具有安全可靠，抗拉抗剪强度高，抗振动。永不松动的特点，广泛用于铁塔、矿山设备、火车厢及铁路设施的制造以及集装箱的制造。

公司主营产品：环槽铆钉、CNC精密零部件、不锈钢铸件,各种冷镦机械加工件,非标异形件、冲压件以及各种机械焊接部件等。

适用领域：铁路交通、汽车、军工、纺织机械、电气、机械设备、航空、高压电器、以及其他工业制造等行业。

主要设备：多功位冷镦机，数控车床，CNC加工中心，磨床，铣床，线切割，摇臂钻，自动焊接机等。

表面处理：六价镀锌，三价镀锌，镀铜，镀镍，达克罗，锌钴镍合金电镀，Magni电镀，碱性无氢电镀。盐雾测试达到800，1000，1200，2000小时。

我司有自动数控车床50多台，数控中心10几台，能够提供最优惠的价格，提供好的品质保障。

长期与国外做OEM配套，生产气动工具、空调设备、汽车等上面的零部件。

Changzhou Ruibo Hardware Technology Co., Ltd. is an enterprise specializing in research development, application and market development of hardware products, precise CNC parts, cold formed and machined products, stainless steel castings, auto parts, industrial fasteners and stampings etc. We own complete testing center, cultivate professional technical team and management team, have adequate internal control system and superior after-sales service.  With the goal of "High Quality, Competitive Price, Sincere and Efficient Service", our company has won a good reputation from various customer group in the field of auto industry, aerospace, railway and bridge, mining industry, engineering plant, hardware industry etc. We have established widely and close partnership with different customers in the United States, Canada, Japan, England, Korea, Chile, India, Thailand and many other countries.  We highly carry forward the enterprise spirit of "Pragmatically, Unite and Strive, Innovation", We will offer best service to our customers, and expect to cooperate with you sincerely, have close communication and common development.

Main Products: 
Lockbolt, Collar, Precise CNC parts, Stainless Steel Castings, various cold formed and machined products, Non-standard parts, Stampings, and all kinds of mechanical welding parts
Applications:
Railway transportation, automobile, military industry, textile machinery, electrical and mechanical equipment, aviation, high voltage apparatus, and other industrial manufacturing industries, etc. 
Main Equipments: 
Multi-functional Cold heading machine, CNC machine, CNC machining center, Grinder, Milling machine, Cutting machine, Drilling machine, Automatic welding machine etc.
Surface Treatment: 
Hexavalent galvanized, Trivalent galvanized, Copper, Nickel, Dacromet, Zn/Co/Ni Alloy Plating, Magni plating, Alkaline plating free of hydrogen. Salt Spray Test can meet 800hr, 1000hr, 1200hr, 2000 hours.

Our Services

• Various styles with different material

• Large stock for fast shipping

• Competitive price with high quality

• Sample order or smaller quantity is ok

• Reliable quality assured

• Best sales service

• Rich exporting experience